## Slide 1: FPGA DESIGN FLOW
Using a 2×2 Matrix Multiplier
Notes: Since matrix multiplication is used almost everywhere in modern computing, we'll use it as our example throughout today's session."

## Slide 2: What do ,ChatGPT, Instagram filters, Image processing and Netflix, YouTube recommendations have in common?

## Slide 3: MATRIX MULTIPLICATION

## Slide 4
Program the FPGA
Implement
Synthesize
Simulate
DESIGN
FLOW : -

## Slide 6
Create a project and add all the Files

## Slide 7
This is what you will get after u press run simulation

## Slide 8
Linting is the process of checking your Verilog code for coding mistakes, bad design practices, and potential bugs before creating the hardware.
It does not create hardware and does not modify your code. It only reports warnings and errors.
Notes: What does it check?
Syntax errors
Unused signals
Width mismatches
Missing default cases
Latch inference
Multiple drivers
Bad coding practices
One-line explanation
Linting is like a grammar checker for Verilog—it checks whether your code follows good design practices before moving to the next stage.

## Slide 9
This is the elaborated design
ROM A
\
→ Multiplier → Accumulator → Result
/
ROM B
Notes: The Elaborated Design shows the logical architecture of our design (RTL). It tells us what modules exist and how they are connected, but it does not show how they will be implemented inside the FPGA. That happens during Synthesis.
Why do we open the Elaborated Design?
It helps us verify that:
All modules are connected correctly.
The hierarchy of the design is correct.
Inputs and outputs are connected as expected.
Data flows through the design correctly.
No module is missing or disconnected.

## Slide 10
Before synthesis update your constraint file according to your code

## Slide 11: What is synthesis?
Synthesis is the process of converting the Verilog RTL code into actual FPGA hardware components such as LUTs, Flip-Flops, DSPs, BRAMs, Multiplexers, and Carry Chains.
What happens during synthesis?
Vivado performs several tasks:
Reads all Verilog modules.
Optimizes the logic.
Removes unused hardware.
Simplifies Boolean expressions.
Infers FPGA resources (LUTs, FFs, DSPs, BRAMs).
Generates a technology-specific netlist.

## Slide 15
Device view of FPGA chip

## Slide 17: NOW LET’S RUN IMPLEMENTATION

## Slide 18
Device view of FPGA after Implementation

## Slide 19
Data flow design after Implementation

## Slide 20
Timing summary after implementation

## Slide 21: Difference between Synthesis and Implementation
Synthesis | Implementation
Converts Verilog into FPGA resources | Places those resources on the FPGA
Creates netlist | Creates physical layout
Maps logic to LUTs, FFs, DSPs | Maps LUTs, FFs, DSPs to exact locations
Estimates timing | Calculates final timing
No routing | Routing completed

## Slide 22: Difference between Synthesized and Implemented Schematic
Synthesized Schematic | Implemented Schematic
Shows logical hardware | Shows placed and routed hardware
FPGA primitives inferred | FPGA primitives physically located
No routing | Routing completed
Estimated timing | Actual timing
Before placement | After placement