## Slide 1
MATRIX MULTIPLICATION USING BRAM

## Slide 2
Add all required files

## Slide 3: Press IP Catalog and search Block Memory Generator

## Slide 4
Remember the name of the component has to be same as what is used in the Verilog code of multiplier portion of the code which is bramAB

## Slide 5
In Port A options change write width to 32 bits and change enable port type to always enable

## Slide 6
In other options, enable load init files as bram A and B shd have the data that’s the matrix with in them.

## Slide 7: Just save the file as anything you like
Since we don’t have that file click on edit and then yes

## Slide 8: The values you give to the matrix as the matrix is 3x3 give atleast 9 values whatever after 9 is unused and then just save it and close it

## Slide 9: This is the summary where we can understand the latency and bram resources and press ok
Click on global and then generate
This will synthesis the design for you and add it to the design

## Slide 10: Now you can see the icon next to bram A and B indicating its not absent now same way add the multiplier also

## Slide 11: Search for multiplier in ip catalog and double click it

## Slide 12: Data type :- unsigned wdith = 32 bits

## Slide 13: Multipliers can either be implemented using LUTs or DSP Slices which are nothing but hardware blocks that are optimized for this purpose or you can simply use LUTs let us use DSP slices for this example either way it doesn’t change the functionality

## Slide 14: In output and controls as o/p shd also be 32 bits. Press use custom o/p width and then make it 31 down to 0 we want pipeline stages to begin with 0 and you can see the clk will vanish as this is combinational logic not a sequential logic and press ok

## Slide 15: Global and generate now you can see in files that even multiplier has also got that icon

## Slide 16: To see missing files just press on that icon and expand it you will get to see all the missing files as we can see adder is missing now the same way lets create an adder instance from ip catalog

## Slide 17: Make all the inputs unsigned and width 32 bit and latency to be 0 as we need it to be combinational block

## Slide 18: In control we don’t need clock so disable that and for the purposes of this implementation there is a need to bypass the adder on certain cycles. Press ok and Generate

## Slide 19: Now to create instance for BramC we shd name it as same as it is instantiated in the parent file which is adder file same way search block memory in ip catalog and change the instance as BRAM_C

## Slide 20: Change write width to 32 and change enable port to always enabled

## Slide 21: In other options we don’t need to add any file for it as we are using this bramC to write our output then press ok and global and generate

## Slide 22: So first time when we run we have just created a multiplier with no pipelining so comment all the lines which have written for pipelined and uncomment the lines which is written for unpipelined then save the file
Now check your constraint file if all the pins are instantiated and after that the code which is given is used for both the pipelined and unpipelined versions

## Slide 23: Once you have done this is how it will look and then now press run simulation

## Slide 24: This is the waveform you get after simulating we are reading the values from the switches and whatever address we give that address is been read that Is matrix C on to the LEDs now RUN SYNTHESIS

## Slide 25: After you run synthesis check and run post synthesis simulation and confirm that the generated has the same netlist has the same functionality as you expect and check the waveform

## Slide 26
To check timing of the design press report timing summary and press ok

## Slide 27: As this is unpipelined version of the code we know for a fact that 10ns is not sufficient we have –ve WNS which means that its not able to finish all the operations within the 10ns period mentioned

## Slide 28: To see which path is not able to complete just press on the WNS here is -7ns this is what you get and to see the schematic of particular path select the path and just click on the highlighted icon

## Slide 30: To explore more about the path just minimize them and zoom in The path is from bram going to the multiplier and then going to the adder inside which we have a register this is the trublsome path which is getting us WNS –VE

## Slide 31: ONE solution this is increase the clock period by pressing on edit timing constraints

## Slide 32: Now increase the clock period by 8ns as that’s what we got in WNS as -7.087ns make it 12ns and click on apply and rerun
Now the issue is solved as you can see there is no violation

## Slide 33: But we don’t want to change the total time period our job is to keep it 10ns period or infact lesser than that so that’s where we use PIPELINED code comes now go back to the multiplier code go to the sources we have to change the multiplier instance

## Slide 34: Double click on this make pipeline stages 5 and press ok and generate

## Slide 35: Having generating these files we need to change the code as well so in multiplier part A just uncomment all the pipeline version and comment all the unpipelined version of code and save it

## Slide 36: Now run simulation and check the functionality and then run synthesis and open the synthesized design check the timing response this time we don’t see the failure by this we can increase the clk frequency without any issue or reduce the clk period just press edit timing constraint

## Slide 37: As the slack is 8ns we can decrease the period to 4ns now rerun and u will see 0.77ns by this we can see approx 3.77ns Is the best clk period we can get by only pipelining the multiplier

## Slide 38: We can further improve this by identifying the critical path which is taking less time so press on the 0.77ns and then select a path and open the schematic

## Slide 39: If you zoom in and minimize some blocks you will understand that entire 32 bit addition is been completed in the single cycle and then being written to the register THAT IS THE CRITICAL PATH

## Slide 40: Now how do we improve further ? Just pipeline the adder also so, change the code accordingly to ensure that it works with this new pipeline which you guys can explore Now let us look into utilization report

## Slide 41: UTILIZATION REPORT

## Slide 42
GENERATE BITSTREAM

## Slide 43: NOW you can program it on FPGA and look at the board to see the output